  INTERRUPT: EXTI0
  INTERRUPT: EXTI1
  INTERRUPT: TIM14
  INTERRUPT: TIM3
SYSTEM OVERVIEW:

12V Battery
5V 4A
Regulator
Stepper Motor
JETSON NANO
STM32F051
U
A
R
T
STEP AND DIRECTION CONTROL
WEBCAM VIDEO FEED

MOTOR CONTROLLER: STM32F051

GLOBAL VARS:
#define width 320

volatile uint8_t DMA_BUFFER[6]; //6bytes of data to be sent via dma
volatile uint8_t SEND_BUFFER[6]; // 6 byte to be stored before sending to dma, updated every 90hz

volatile uint32_t microseconds; //unit is 2us not 1us

volatile bool status = 0; //used to keep step status
volatile bool isCalibrated = 0;
volatile bool dir = 0;

volatile uint16_t current_steps = 1200;
volatile uint16_t target_steps = 300; //max: 1200 current_steps == 180*

//as received from the uart
volatile uint16_t x_center;
volatile bool new_x_center_flag;

//will be used to keep the incoming uart data
#define INPUT_BUFFER_MAX_LENGTH 2
volatile uint8_t INPUT_BUFFER[INPUT_BUFFER_MAX_LENGTH]; //max 2 bytes
volatile uint8_t input_buffer_index = 0;

volatile bool time_calibrate_flag = 0; //used if the time zero button is pressed to reset the time on the next 90Hz sending interrupt
volatile uint32_t last_trigger_exti0_1 = 0; //used for debouncing the btn
volatile uint32_t last_trigger_exti2_3 = 0; //used for debouncing the btn

FUNCTIONS:
int main(void)

//initialisation functions
void init_TIM3(void);
void init_TIM14(void);
void init_TIM15(void);
void init_TIM16(void);
void init_TIM17(void);

void init_GPIOA(void);
void init_GPIOB(void);
void init_UART1(void);
void init_DMA(void);

//auxiliary functions
void update_motor_control(uint16_t current_steps);
void update_target_steps(uint16_t x_center);
void reset_time(void);

//Interrupt Handlers
void TIM14_IRQHandler(void) //frequency modulated for motor stepping
void TIM15_IRQHandler(void) // @90Hz send data to UART TX using DMA
void TIM16_IRQHandler(void) // @500kHz increment microseconds
void TIM17_IRQHandler(void) // one shot timer for buzzing
void TIM3_IRQHandler(void) // @32Hz update_motor_control
void EXTII0_1_IRQHandler(void)
void EXTII2_3_IRQHandler(void)//used unit step testing on PA1
void USART1_IRQHandler(void)

PROGRAM FLOW STM32F051:

START:
motor rotate anticlockwise
Reset current_steps = 0
Main loop
Set reset_tim_flag=1
to tell TIM15 to reset microseconds=0
on the next TIM15 interrupt
Toggle step pin (PB0) and update current_steps
depending on dir
Compare current_steps to target_steps and update
The frequency of TIM14 depending on error
And also update dir
        INTERRUPT: TIM16
        INTERRUPT: TIM15
   INTERRUPT: UART1_RXNE
For timekeeping
microseconds++
NOTE: microseconds unit is 2us not 1us
because TIM16 is 500kHz
Every 90Hz load data packet
2 bytes current_step + 4bytes microseconds
Into DMA memory buffer to send to UART TX
if(reset_time_flag){
    Microseconds = 0;
    Start buzzer;
}
Read available byte to INPUT_BUFFER.
When 2bytes in INPUT_BUFFER,
convert it to uint16_t.
update_target_steps() using the received value
as xcenter
update_target_steps

update_motor_control
X

target_steps
xcenter

current_steps
-
OBJECT DETECTION: JETSON NANO

GLOBAL VARS:

microseconds = []
#holds all the timestamps received from uart.
#NOTE: each unit is 2 microseconds not 1 since the counter freq of the stm32 is 500kHz not 1MHz due to some issue I couldnt get the timer (TIM16) to 1MHz. total runtime before timestasmps overflow is ~ 240min

steps = []
# holds the received steps receioved from thr uaurt at the correspomding timestamp
display_size = (320,240) #(width, height) 320, 240
uart = serial.Serial("/dev/ttyTHS1", baudrate=115200)
FUNCTIONS:

def object_detection(x_center_conn):
#will run on a seperate process and is using the NVIDIA detectNet inference engine to detect an object in the frame using the ssd-mobilenet-v2 network (API from https://github.com/dusty-nv/jetson-inference)

PROGRAM FLOW:

START:

Process1

Process2

Receive xcenter from pipe
Send to uart
if(UART.in_waiting):
    Receive from UART

main_xcenter_conn	PIPE	detect_xcenter_conn
Inference using “detectNet”

if(person detected):
    Send xcenter to pipe
    to main process